## Slide 1: Bits, Bytes, and Integers 15-213: Introduction to Computer Systems 2nd and 3rd Lectures, Sep. 3 and Sep. 8, 2015
Instructors:
Randal E. Bryant and David R. O’Hallaron

## Slide 2: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 3: Everything is bits
Each bit is 0 or 1
By encoding/interpreting sets of bits in various ways
  Computers determine what to do (instructions)
  … and represent and manipulate numbers, sets, strings, etc…
Why bits? Electronic Implementation
  Easy to store with bistable elements
  Reliably transmitted on noisy and inaccurate wires
0.0V
0.2V
0.9V
1.1V
0
1
0

## Slide 4: For example, can count in binary
Base 2 Number Representation
  Represent 1521310 as 111011011011012
  Represent 1.2010 as 1.0011001100110011[0011]…2
  Represent 1.5213 X 104 as 1.11011011011012 X 213

## Slide 5: Encoding Byte Values
Byte = 8 bits
  Binary 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal 0016 to FF16
    Base 16 number representation
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    Write FA1D37B16 in C as
      0xFA1D37B
      0xfa1d37b
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 6: Example Data Representations
C Data Type | Typical 32-bit | Typical 64-bit | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
long double | − | − | 10/16
pointer | 4 | 8 | 8

## Slide 7: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 8: Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
And
A&B = 1 when both A=1 and B=1
Or
A|B = 1 when either A=1 or B=1
Not
~A = 1 when A=0
Exclusive-Or (Xor)
A^B = 1 when either A=1 or B=1, but not both

## Slide 9: General Boolean Algebras
Operate on Bit Vectors
  Operations applied bitwise
All of the Properties of Boolean Algebra Apply
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01000001
01111101
00111100
10101010

## Slide 10: Example: Representing & Manipulating Sets
Representation
  Width w bit vector represents subsets of {0, …, w–1}
  aj = 1 if j ∈ A
    01101001 { 0, 3, 5, 6 }
    76543210
    01010101 { 0, 2, 4, 6 }
    76543210
Operations
  & Intersection 01000001 { 0, 6 }
  | Union 01111101 { 0, 2, 3, 4, 5, 6 }
  ^ Symmetric difference 00111100 { 2, 3, 4, 5 }
  ~ Complement 10101010 { 1, 3, 5, 7 }

## Slide 11: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 ➙ 0xBE
    ~010000012 ➙ 101111102
  ~0x00 ➙ 0xFF
    ~000000002 ➙ 111111112
  0x69 & 0x55 ➙ 0x41
    011010012 & 010101012 ➙ 010000012
  0x69 | 0x55 ➙ 0x7D
    011010012 | 010101012 ➙ 011111012

## Slide 12: Contrast: Logic Operations in C
Contrast to Logical Operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type)
  !0x41 ➙ 0x00
  !0x00 ➙ 0x01
  !!0x41 ➙ 0x01
  0x69 && 0x55 ➙ 0x01
  0x69 || 0x55 ➙ 0x01
  p && *p (avoids null pointer access)
Early Termination

## Slide 13: Contrast: Logic Operations in C
Contrast to Logical Operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type)
  !0x41 ➙ 0x00
  !0x00 ➙ 0x01
  !!0x41 ➙ 0x01
  0x69 && 0x55 ➙ 0x01
  0x69 || 0x55 ➙ 0x01
  p && *p (avoids null pointer access)
Watch out for && vs. & (and || vs. |)…
one of the more common oopsies in
C programming

## Slide 14: Shift Operations
Left Shift: x << y
  Shift bit-vector x left y positions
      Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on left
Undefined Behavior
  Shift amount < 0 or ≥ word size
01100010
Argument x
00010000
<< 3
00011000
Log. >> 2
00011000
Arith. >> 2
10100010
Argument x
00010000
<< 3
00101000
Log. >> 2
11101000
Arith. >> 2
00010000
00010000
00011000
00011000
00011000
00011000
00010000
00101000
11101000
00010000
00101000
11101000

## Slide 15: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings
Summary

## Slide 16: Encoding Integers
short int x = 15213;
short int y = -15213;
C short 2 bytes long
Sign Bit
  For 2’s complement, most significant bit indicates sign
    0 for nonnegative
    1 for negative
Unsigned
Two’s Complement
Sign
Bit

## Slide 17: Two-complement Encoding Example (Cont.)
x = 15213: 00111011 01101101
y = -15213: 11000100 10010011

## Slide 18: Numeric Ranges
Unsigned Values
  UMin = 0
    000…0
  UMax = 2w – 1
    111…1
Two’s Complement Values
  TMin = –2w–1
    100…0
  TMax = 2w–1 – 1
    011…1
Other Values
  Minus 1
    111…1
Values for W = 16

## Slide 19: Values for Different Word Sizes
Observations
  |TMin | = TMax + 1
    Asymmetric range
  UMax = 2 * TMax + 1
C Programming
  #include <limits.h>
  Declares constants, e.g.,
    ULONG_MAX
    LONG_MAX
    LONG_MIN
  Values platform specific

## Slide 20: Unsigned & Signed Numeric Values
Equivalence
  Same encodings for nonnegative values
Uniqueness
  Every bit pattern represents unique integer value
  Each representable integer has unique bit encoding
 Can Invert Mappings
  U2B(x) = B2U-1(x)
    Bit pattern for unsigned integer
  T2B(x) = B2T-1(x)
    Bit pattern for two’s comp integer
X
B2T(X)
B2U(X)
0000
0
0001
1
0010
2
0011
3
0100
4
0101
5
0110
6
0111
7
–8
8
–7
9
–6
10
–5
11
–4
12
–3
13
–2
14
–1
15
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7

## Slide 21: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 22: Mapping Between Signed & Unsigned
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X
U2T
U2B
B2T
Two’s Complement
Unsigned
Maintain Same Bit Pattern
ux
x
X
Mappings between unsigned and two’s complement numbers: Keep bit representations and reinterpret

## Slide 23: Mapping Signed  Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
U2T
T2U
Absolute value:
| T | = ~ ( T – 1)
Due to the zero
The Absolute value
of Tmin is itself

## Slide 24: Mapping Signed  Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
=
+/- 16

## Slide 25: Relation between Signed & Unsigned
+
+
+
+
+
+
• • •
-
+
+
+
+
+
• • •
ux
x
w–1
0
Large negative weight
becomes
Large positive weight
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X

## Slide 26: Conversion Visualized
0
TMax
TMin
–1
–2
0
UMax
UMax – 1
TMax
TMax + 1
2’s Complement Range
Unsigned
Range
2’s Comp.  Unsigned
  Ordering Inversion
  Negative  Big Positive

## Slide 27: Signed vs. Unsigned in C
Constants
  By default are considered to be signed integers
  Unsigned if have “U” as suffix
    0U, 4294967259U
Casting
  Explicit casting between signed & unsigned same as U2T and T2U
    int tx, ty;
    unsigned ux, uy;
    tx = (int) ux;
    uy = (unsigned) ty;
  Implicit casting also occurs via assignments and procedure calls
    tx = ux;
    uy = ty;
If either argument is unsigned then it interprets remaining arguments as being unsigned

## Slide 28: Casting Surprises
  0 0U == unsigned
  -1 0 < signed
  -1 0U > unsigned
  2147483647 -2147483648 > signed
  2147483647U -2147483648 < unsigned
  -1 -2 > signed
  (unsigned) -1 -2 > unsigned
  2147483647 2147483648U < unsigned
  2147483647 (int) 2147483648U > signed
Expression Evaluation
  If there is a mix of unsigned and signed in single expression, signed values implicitly cast to unsigned
  Including comparison operations <, >, ==, <=, >=
  Examples for W = 32: TMIN = -2,147,483,648 , TMAX = 2,147,483,647
Constant1 Constant2 Relation Evaluation
  0 0U
  -1 0
  -1 0U
  2147483647 -2147483647-1
  2147483647U -2147483647-1 (TMin)
  -1 -2
  (unsigned)-1 -2
  2147483647 2147483648U
  2147483647 (int) 2147483648U
Tmin = -Tmax-1
Umax = 2*Tmax + 1

## Slide 29: Summary Casting Signed ↔ Unsigned: Basic Rules
Bit pattern is maintained
But reinterpreted
Can have unexpected effects: adding or subtracting 2w
Expression containing signed and unsigned int
  int is cast to unsigned!!
There do not have any difference when ALU do calculations between unsigned and signed number.
Only the representation has some difference
Will output positive number from Umax to 0

## Slide 30: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings
Will output numbers from 0 to Tmin
Will treat that statement as an unsigned number

## Slide 31: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k

## Slide 32: Sign Extension Example
Converting from smaller to larger integer data type
C automatically performs sign extension
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011

## Slide 33: Summary: Expanding, Truncating: Basic Rules
Expanding (e.g., short int to int)
  Unsigned: zeros added
  Signed: sign extension
  Both yield expected result
Truncating (e.g., unsigned to unsigned short)
  Unsigned/signed: bits are truncated
  Result reinterpreted
  Unsigned: mod operation
  Signed: similar to mod
  For small numbers yields expected behavior

## Slide 34: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
Representations in memory, pointers, strings
Summary

## Slide 35: Unsigned Addition
Standard Addition Function
  Ignores carry output
Implements Modular Arithmetic
  s = UAddw(u , v) = u + v mod 2w
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
UAddw(u , v)

## Slide 36: Visualizing (Mathematical) Integer Addition
Integer Addition
  4-bit integers u, v
  Compute true sum Add4(u , v)
  Values increase linearly with u and v
  Forms planar surface
Add4(u , v)
u
v

## Slide 37: Visualizing Unsigned Addition
Wraps Around
  If true sum ≥ 2w
  At most once
0
2w
2w+1
UAdd4(u , v)
u
v
True Sum
Modular Sum
Overflow
Overflow

## Slide 38: Two’s Complement Addition
TAdd and UAdd have Identical Bit-Level Behavior
  Signed vs. unsigned addition in C:
  int s, t, u, v;
  s = (int) ((unsigned) u + (unsigned) v);
  t = u + v
  Will give s == t
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
TAddw(u , v)
Why two’s complement is the most used way of representing signed numbers.
Because the same hardware the same algorithms that are used for doing addition in work for either unsigned or two’s complement numbers

## Slide 39: TAdd Overflow
Functionality
  True sum requires w+1 bits
  Drop off MSB
  Treat remaining bits as 2’s comp. integer
–2w –1
–2w
0
2w –1–1
2w–1
True Sum
TAdd Result
1 000…0
1 011…1
0 000…0
0 100…0
0 111…1
100…0
000…0
011…1
PosOver
NegOver

## Slide 40: Visualizing 2’s Complement Addition
Values
  4-bit two’s comp.
  Range from -8 to +7
Wraps Around
  If sum  2w–1
    Becomes negative
    At most once
  If sum < –2w–1
    Becomes positive
    At most once
TAdd4(u , v)
u
v
PosOver
NegOver

## Slide 41: Multiplication
Goal: Computing Product of w-bit numbers x, y
  Either signed or unsigned
But, exact results can be bigger than w bits
  Unsigned: up to 2w bits
    Result range: 0 ≤ x * y ≤ (2w – 1) 2 = 22w – 2w+1 + 1
  Two’s complement min (negative): Up to 2w-1 bits
    Result range: x * y ≥ (–2w–1)*(2w–1–1) = –22w–2 + 2w–1
  Two’s complement max (positive): Up to 2w bits, but only for (TMinw)2
    Result range: x * y ≤ (–2w–1) 2 = 22w–2
So, maintaining exact results…
  would need to keep expanding word size with each product computed
  is done in software, if needed
    e.g., by “arbitrary precision” arithmetic packages

## Slide 42: Unsigned Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
Implements Modular Arithmetic
  UMultw(u , v) = u · v mod 2w
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
UMultw(u , v)
• • •

## Slide 43: Signed Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
  Some of which are different for signed vs. unsigned multiplication
  Lower bits are the same
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
TMultw(u , v)
• • •

## Slide 44: Power-of-2 Multiply with Shift
Operation
  u << k gives u * 2k
  Both signed and unsigned
Examples
  u << 3 == u * 8
  (u << 5) – (u << 3) == u * 24
  Most machines shift and add faster than multiply
    Compiler generates this code automatically
• • •
0
0
1
0
0
0
•••
u
2k
*
u · 2k
True Product: w+k bits
Operands: w bits
Discard k bits: w bits
UMultw(u , 2k)
•••
k
• • •
0
0
0
•••
TMultw(u , 2k)
0
0
0
•••
•••

## Slide 45: Unsigned Power-of-2 Divide with Shift
Quotient of Unsigned by Power of 2
  u >> k gives  u / 2k 
  Uses logical shift
0
0
1
0
0
0
•••
u
2k
/
u / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
0
0
•••
•••
 u / 2k 
•••
Result:
.
Binary Point
0
0
0
0
•••
0

## Slide 46: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 47: Arithmetic: Basic Rules
Addition:
  Unsigned/signed: Normal addition followed by truncate, same operation on bit level
  Unsigned: addition mod 2w
    Mathematical addition + possible subtraction of 2w
  Signed: modified addition mod 2w (result in proper range)
    Mathematical addition + possible addition or subtraction of 2w
Multiplication:
  Unsigned/signed: Normal multiplication followed by truncate, same operation on bit level
  Unsigned: multiplication mod 2w
  Signed: modified multiplication mod 2w (result in proper range)

## Slide 48: Why Should I Use Unsigned?
Don’t use without understanding implications
  Easy to make mistakes
    unsigned i;
    for (i = cnt-2; i >= 0; i--)
    a[i] += a[i+1];
  Can be very subtle
    #define DELTA sizeof(int)
    int i;
    for (i = CNT; i-DELTA >= 0; i-= DELTA)
    . . .

## Slide 49: Counting Down with Unsigned
Proper way to use unsigned as loop index
    unsigned i;
    for (i = cnt-2; i < cnt; i--)
    a[i] += a[i+1];
See Robert Seacord, Secure Coding in C and C++
  C Standard guarantees that unsigned addition will behave like modular arithmetic
    0 – 1  UMax
Even better
    size_t i;
    for (i = cnt-2; i < cnt; i--)
    a[i] += a[i+1];
  Data type size_t defined as unsigned value with length = word size
  Code will work even if cnt = UMax
  What if cnt is signed and < 0?

## Slide 50: Why Should I Use Unsigned? (cont.)
Do Use When Performing Modular Arithmetic
  Multiprecision arithmetic
Do Use When Using Bits to Represent Sets
  Logical right shift, no sign extension

## Slide 51: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 52: Byte-Oriented Memory Organization
Programs refer to data by address
  Conceptually, envision it as a very large array of bytes
    In reality, it’s not, but can think of it that way
  An address is like an index into that array
    and, a pointer variable stores an address
Note: system provides private address spaces to each “process”
  Think of a process as a program being executed
  So, a program can clobber its own data, but not that of others
• • •
00•••0
FF•••F

## Slide 53: Machine Words
Any given computer has a “Word Size”
  Nominal size of integer-valued data
    and of addresses
  Until recently, most machines used 32 bits (4 bytes) as word size
    Limits addresses to 4GB (232 bytes)
  Increasingly, machines have 64-bit word size
    Potentially, could have 18 EB (exabytes) of addressable memory
    That’s 18.4 X 1018
  Machines still support multiple data formats
    Fractions or multiples of word size
    Always integral number of bytes
Trick
Approximate value
2^10 = 1024
10^3 = 1000
In real machines (64 bits) program are allowed to using 47 bits address space
Which is 128 * 10^12 = 16 tera bytes
1 million = 10^6 (MHZ)
1 billion = 1000 million = 10^9 (GHZ)
10^12 = 1 tera = 1000 billion (THZ)

## Slide 54: Word-Oriented Memory Organization
Addresses Specify Byte Locations
  Address of first byte in word
  Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008

## Slide 55: Example Data Representations
C Data Type | Typical 32-bit | Typical 64-bit | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
long double | − | − | 10/16
pointer | 4 | 8 | 8

## Slide 56: Byte Ordering
So, how are the bytes within a multi-byte word ordered in memory?
Conventions
  Big Endian: Sun, PPC Mac, Internet
    Least significant byte has highest address
  Little Endian: x86, ARM processors running Android, iOS, and Windows
    Least significant byte has lowest address

## Slide 57: Byte Ordering Example
Example
  Variable x has 4-byte value of 0x01234567
  Address given by &x is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01

## Slide 58: Representing Integers
Decimal: 15213
Binary: 0011 1011 0110 1101
Hex: 3 B 6 D
6D
3B
00
00
IA32, x86-64
3B
6D
00
00
Sun
int A = 15213;
93
C4
FF
FF
IA32, x86-64
C4
93
FF
FF
Sun
Two’s complement representation
int B = -15213;
long int C = 15213;
00
00
00
00
6D
3B
00
00
x86-64
3B
6D
00
00
Sun
6D
3B
00
00
IA32

## Slide 59: Examining Data Representations
Code to Print Byte Representation of Data
  Casting pointer to unsigned char * allows treatment as a byte array
Printf directives:
%p: Print pointer
%x: Print Hexadecimal
typedef unsigned char *pointer;
void show_bytes(pointer start, size_t len){
size_t i;
for (i = 0; i < len; i++)
printf(”%p\t0x%.2x\n",start+i, start[i]);
printf("\n");
}

## Slide 60: show_bytes Execution Example
int a = 15213;
printf("int a = 15213;\n");
show_bytes((pointer) &a, sizeof(int));
Result (Linux x86-64):
int a = 15213;
0x7fffb7f71dbc 6d
0x7fffb7f71dbd 3b
0x7fffb7f71dbe 00
0x7fffb7f71dbf 00

## Slide 61: Representing Pointers
Different compilers & machines assign different locations to objects
Even get different results each time run program
int B = -15213;
int *P = &B;
x86-64
Sun
IA32
EF
FF
FB
2C
AC
28
F5
FF
3C
1B
FE
82
FD
7F
00
00

## Slide 62: Representing Strings
char S[6] = "18213";
Strings in C
  Represented by array of characters
  Each character encoded in ASCII format
    Standard 7-bit encoding of character set
    Character “0” has code 0x30
      Digit i has code 0x30+i
  String should be null-terminated
    Final character = 0
Compatibility
  Byte ordering not an issue
IA32
Sun
31
38
32
31
33
00
31
38
32
31
33
00
The C standard is still back in the days of only supporting the ASCII format

## Slide 63: Integer C Puzzles
x < 0  ((x*2) < 0)
ux >= 0
x & 7 == 7  (x<<30) < 0
ux > -1
x > y  -x < -y
x * x >= 0
x > 0 && y > 0  x + y > 0
x >= 0  -x <= 0
x <= 0  -x >= 0
(x|-x)>>31 == -1
ux >> 3 == ux/8
x >> 3 == x/8
x & (x-1) != 0
int x = foo();
int y = bar();
unsigned ux = x;
unsigned uy = y;
Initialization
- Tmin = Tmin

## Slide 64: Bonus extras

## Slide 65: Application of Boolean Algebra
Applied to Digital Systems by Claude Shannon
  1937 MIT Master’s Thesis
  Reason about networks of relay switches
    Encode closed switch as 1, open switch as 0
A
~A
~B
B
Connection when
A&~B | ~A&B
A&~B
~A&B
= A^B

## Slide 66: Binary Number Property
w = 0:
  1 = 20
Assume true for w-1:
  1 + 1 + 2 + 4 + 8 + … + 2w-1 + 2w = 2w + 2w = 2w+1
Claim
1 + 1 + 2 + 4 + 8 + … + 2w-1 = 2w
= 2w

## Slide 67: Code Security Example
Similar to code found in FreeBSD’s implementation of getpeername
There are legions of smart people trying to find vulnerabilities in programs
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}

## Slide 68: Typical Usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, MSIZE);
printf(“%s\n”, mybuf);
}

## Slide 69: Malicious Usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, -MSIZE);
. . .
}
/* Declaration of library function memcpy */
void *memcpy(void *dest, void *src, size_t n);

## Slide 70: Mathematical Properties
Modular Addition Forms an Abelian Group
  Closed under addition
    0  UAddw(u , v)  2w –1
  Commutative
    UAddw(u , v) = UAddw(v , u)
  Associative
    UAddw(t, UAddw(u , v)) = UAddw(UAddw(t, u ), v)
  0 is additive identity
    UAddw(u , 0) = u
  Every element has additive inverse
    Let UCompw (u ) = 2w – u UAddw(u , UCompw (u )) = 0

## Slide 71: Mathematical Properties of TAdd
Isomorphic Group to unsigneds with UAdd
  TAddw(u , v) = U2T(UAddw(T2U(u ), T2U(v)))
    Since both have identical bit patterns
Two’s Complement Under TAdd Forms a Group
  Closed, Commutative, Associative, 0 is additive identity
  Every element has additive inverse

## Slide 72: Characterizing TAdd
Functionality
  True sum requires w+1 bits
  Drop off MSB
  Treat remaining bits as 2’s comp. integer
(NegOver)
(PosOver)
u
v
< 0
> 0
< 0
> 0
Negative Overflow
Positive Overflow
TAdd(u , v)
2w
2w

## Slide 73: Negation: Complement & Increment
Claim: Following Holds for 2’s Complement
  ~x + 1 == -x
Complement
  Observation: ~x + x == 1111…111 == -1
Complete Proof?
1
0
0
1
0
1
1
1
x
0
1
1
0
1
0
0
0
~x
+
1
1
1
1
1
1
1
1
-1

## Slide 74: Complement & Increment Examples
x = 15213
x = 0

## Slide 75: Code Security Example #2
SUN XDR library
  Widely used library for transferring data between machines
void* copy_elements(void *ele_src[], int ele_cnt, size_t ele_size);
ele_src
malloc(ele_cnt * ele_size)

## Slide 76: XDR Code
void* copy_elements(void *ele_src[], int ele_cnt, size_t ele_size) {
/*
* Allocate buffer for ele_cnt objects, each of ele_size bytes
* and copy from locations designated by ele_src
*/
void *result = malloc(ele_cnt * ele_size);
if (result == NULL)
/* malloc failed */
return NULL;
void *next = result;
int i;
for (i = 0; i < ele_cnt; i++) {
/* Copy object i to destination */
memcpy(next, ele_src[i], ele_size);
/* Move pointer to next memory region */
next += ele_size;
}
return result;
}

## Slide 77: XDR Vulnerability
What if:
  ele_cnt = 220 + 1
  ele_size = 4096 = 212
  Allocation = ??
How can I make this function secure?
malloc(ele_cnt * ele_size)

## Slide 78: Compiled Multiplication Code
leaq (%rax,%rax,2), %rax
salq $2, %rax
C compiler automatically generates shift/add code when multiplying by constant
long mul12(long x)
{
return x*12;
}
t <- x+x*2
return t << 2;
C Function
Compiled Arithmetic Operations
Explanation

## Slide 79: Compiled Unsigned Division Code
shrq $3, %rax
Uses logical shift for unsigned
For Java Users
  Logical shift written as >>>
unsigned long udiv8
(unsigned long x)
{
return x/8;
}
# Logical shift
return x >> 3;
C Function
Compiled Arithmetic Operations
Explanation

## Slide 80: Signed Power-of-2 Divide with Shift
Quotient of Signed by Power of 2
  x >> k gives  x / 2k 
  Uses arithmetic shift
  Rounds wrong direction when u < 0
0
0
1
0
0
0
•••
x
2k
/
x / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
•••
•••
RoundDown(x / 2k)
•••
Result:
.
Binary Point
0
•••

## Slide 81: Correct Power-of-2 Divide
Quotient of Negative Number by Power of 2
  Want  x / 2k  (Round Toward 0)
  Compute as  (x+2k-1)/ 2k 
    In C: (x + (1<<k)-1) >> k
    Biases dividend toward 0
Case 1: No rounding
Divisor:
Dividend:
0
0
1
0
0
0
•••
u
2k
/
 u / 2k 
•••
k
1
•••
0
0
0
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
1
1
•••
1
•••
1
1
1
•••
    Biasing has no effect

## Slide 82: Correct Power-of-2 Divide (Cont.)
Divisor:
Dividend:
Case 2: Rounding
0
0
1
0
0
0
•••
x
2k
/
 x / 2k 
•••
k
1
•••
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
•••
•••
    Biasing adds 1 to final result
•••
Incremented by 1
Incremented by 1

## Slide 83: Compiled Signed Division Code
testq %rax, %rax
js L4
L3:
sarq $3, %rax
ret
L4:
addq $7, %rax
jmp L3
Uses arithmetic shift for int
For Java Users
  Arith. shift written as >>
long idiv8(long x)
{
return x/8;
}
if x < 0
x += 7;
# Arithmetic shift
return x >> 3;
C Function
Compiled Arithmetic Operations
Explanation

## Slide 84: Arithmetic: Basic Rules
Unsigned ints, 2’s complement ints are isomorphic rings: isomorphism = casting
Left shift
  Unsigned/signed: multiplication by 2k
  Always logical shift
Right shift
  Unsigned: logical shift, div (division + round to zero) by 2k
  Signed: arithmetic shift
    Positive numbers: div (division + round to zero) by 2k
    Negative numbers: div (division + round away from zero) by 2k Use biasing to fix

## Slide 85: Properties of Unsigned Arithmetic
Unsigned Multiplication with Addition Forms Commutative Ring
  Addition is commutative group
  Closed under multiplication
    0  UMultw(u , v)  2w –1
  Multiplication Commutative
    UMultw(u , v) = UMultw(v , u)
  Multiplication is Associative
    UMultw(t, UMultw(u , v)) = UMultw(UMultw(t, u ), v)
  1 is multiplicative identity
    UMultw(u , 1) = u
  Multiplication distributes over addtion
    UMultw(t, UAddw(u , v)) = UAddw(UMultw(t, u ), UMultw(t, v))

## Slide 86: Properties of Two’s Comp. Arithmetic
Isomorphic Algebras
  Unsigned multiplication and addition
    Truncating to w bits
  Two’s complement multiplication and addition
    Truncating to w bits
Both Form Rings
  Isomorphic to ring of integers mod 2w
Comparison to (Mathematical) Integer Arithmetic
  Both are rings
  Integers obey ordering properties, e.g.,
    u > 0  u + v > v
    u > 0, v > 0  u · v > 0
  These properties are not obeyed by two’s comp. arithmetic
    TMax + 1 == TMin
    15213 * 30426 == -10030 (16-bit words)

## Slide 87: Reading Byte-Reversed Listings
Address Instruction Code Assembly Rendition
8048365: 5b pop %ebx
8048366: 81 c3 ab 12 00 00 add $0x12ab,%ebx
804836c: 83 bb 28 00 00 00 00 cmpl $0x0,0x28(%ebx)
Disassembly
  Text representation of binary machine code
  Generated by program that reads the machine code
Example Fragment
Deciphering Numbers
  Value: 0x12ab
  Pad to 32 bits: 0x000012ab
  Split into bytes: 00 00 12 ab
  Reverse: ab 12 00 00